## Slide 1: IPv6 Einführung
Notes: This is the first of 2 PowerPoint presentations that introduce IPv6. The two presentations combined provide information on the purpose and benefits of IPv6 as well as an explanation of the addressing structure.
NOTE: Most of the slides have notes to provide additional detail and background information for student handouts if desired and these can also be used as lecture points by the instructor.

## Slide 2: IPv6 Addressing Overview
IPv6 increases the number of address bits by a factor of 4, from 32 to 128, providing a very large number of addressable nodes.
IPv4 = 32 bits |  |  | 
11111111.11111111.11111111.11111111 |  |  | 
IPv6 = 128 bits |  |  | 
11111111.11111111.11111111.11111111 | 11111111.11111111.11111111.11111111 | 11111111.11111111.11111111.11111111 | 11111111.11111111.11111111.11111111
2128 = 340.282.366.920.938.463.463.374.607.431.768.211.456
Notes: With IPv4, some number of bits on the left side of the 32 bit address represent the network and possibly the subnet.
The remaining bits represent a host on that network/subnet.
With IPv6, normally the first 64 bits represent the network/subnet address and the remaining 64 bits represent the host address. This will be covered in greater detail later.

## Slide 3: IPv6 Address Space Overview
Prefix Hex Value | Use
0000 to 00FF | Unspecified Loopback IPv4-compatible
0100 to 01FF | Unassigned (0.38 % of IPv6 space)
0200 to 03FF | NSAP Network Service AP)
0400 to 1FFF | Unassigned (~11% of IPv6 space)
2000 to 3FFF | Aggregatable global unicast (12.5%)
4000 to FE7F (Huge) | Unassigned (~75% of IPv6 space)
FE80 to FEBF | Link-local
FC00 to FCFF | Unique-local
FF00 to FFFF | Multicast
Note: IPv6 Internet uses 2001::/3 which is < 2% of IPv6 address space
Notes: As we have seen in Lesson 1, the IPv6 address space is very large.
The first four Hexadecimal digits of the prefix help to classify the various blocks of IPv6 addresses. The ability to identify an address type by its prefix is essential to understanding IPv6.
In the table, the prefixes highlighted in red are important ones to remember.
The largest block of assignable addresses, from Hex 2000 to Hex 3FFF, is known as the aggregatable global unicast range which represents approximately 12.5% of the total IPv6 address space. From this range, only addresses from 2001::/3 are currently being assigned by IANA for public use on IPv6 Internet. This is less than 2% of the total IPv6 address space.

## Slide 4: Special IPv6 Addresses
IPv6 Address | Description
::/0 | All networks and used when specifying a default static route. It is equivalent to the IPv4 quad-zero (0.0.0.0)
::/128 | Unspecified address and is initially assigned to a host when it first resolves its local link address
::1/128 | Loopback address of local host Equivalent to 127.0.0.1 in IPv4
FE80::/10 | Link-local unicast address Similar to the Windows autoconfiguration IP address of 169.254.x.x
FF00::/8 | Multicast addresses
All other addresses | Global unicast address
Notes: Some of the special IPv6 addresses and prefixes are similar to IPv4.
The ones shown here are particularly useful to remember.
For example, IPv6 address ::/0 is analogous to IPv4 quad zero address 0.0.0.0 0.0.0.0, for use in defining static default routes.
IPv6 address ::1/128 is analogous to IPv4 local host loopback address 127.0.0.1.

## Slide 5: IPv6 Prefix Allocation Hierarchy and Policy Example
Site
/48
Site
/48
ISP
/32
ISP
/32
IANA
2001::/3
APNIC
::/12 to::/23
AfriNIC
::/12 to::/23
ARIN
::/12 to::/23
LACNIC
::/12 to::/23
RIPE NCC
::/12 to::/23
ISP
/32
Site
/48
Site
/48
Site
/48
ISP
/32
ISP
/32
ISP
/32
Site
/48
Site
/48
Site
/48
ISP
/32
ISP
/32
ISP
/32
Site
/48
Site
/48
Site
/48
ISP
/32
ISP
/32
ISP
/32
Site
/48
Site
/48
Site
/48
ISP
/32
ISP
/32
ISP
/32
Site
/48
Notes:   IPv6 address space is allocated in a hierarchical manner as shown here:
  IANA allocates from the total 2001::/3 global IPv6 unicast address space to regional registries such as APNIC and RIPE.
  Each regional registry gets a /23 prefix from IANA (although a larger address space can be requested).
  The registry typically allocates a /32 prefix to an IPv6 ISP.
  Then the ISP allocates a /48 prefix to each customer (or potentially /64 for a local network or /128 for a single host).

## Slide 6: IPv6 Global Unicast Address
The current IANA global routing prefix uses the range that starts with binary 0010 (2000::/3).
Global Routing Prefix
Subnet
ID
Interface ID
2001 0010 | 0008 |  |  | 21B:D5FF:FE5B:A408
/23
Registry
/32
ISP Prefix
/48
Site Prefix
/64
Subnet Prefix
Notes:   The current IANA global routing prefix uses the range that starts with binary 0010 (2000::/3).
  Addresses with a prefix of 2000::/3 (0010) to E000::/3 (1110) are required to have 64-bit interface IDs in the extended universal identifier (EUI)-64 format.
  IPv6 prefix allocation is defined by policies at IANA and the regional registries.

## Slide 7: IPv6 Global Unicast Address
The current IANA global routing prefix uses the range that starts with binary 0010 (2000::/3).
Global Routing Prefix
Subnet
ID
Interface ID
2001 0010 | 0008 |  |  | 21B:D5FF:FE5B:A408
/23
Registry
/32
ISP Prefix
/48
Site Prefix
/64
Subnet Prefix
Notes:   The current IANA global routing prefix uses the range that starts with binary 0010 (2000::/3).
  Addresses with a prefix of 2000::/3 (0010) to E000::/3 (1110) are required to have 64-bit interface IDs in the extended universal identifier (EUI)-64 format.
  IPv6 prefix allocation is defined by policies at IANA and the regional registries.

## Slide 8: IPv6 Global Unicast Address
The subnet ID can be used by an organization to create their own local addressing hierarchy.
Global Routing Prefix
Subnet
ID
Interface ID
2001 0010 | 0008 |  |  | 21B:D5FF:FE5B:A408
/23
Registry
/32
ISP Prefix
/48
Site Prefix
/64
Subnet Prefix
Notes: The subnet ID can be used by an organization to create their own local addressing hierarchy.
This 16-bit field allows up to 65,536 individual subnets.
This number of subnets is comparable to an IPv4 network address such as 10.0.0.0/8 with 16 bits of subnetting using a /24 mask, however the IPv4 network/subnet combination will allow only 256 hosts per subnet and the IPv6 combination allows a huge number of hosts per subnet (2 to the 64th power).

## Slide 9: IPv6 Address Allocation Process
Notes: This graphic depicts the address allocation process starting with the entire IPv6 global unicast address space and ending with a single 128-bit IPv6 address for a host on a LAN.

## Slide 10: IPv6 Address Specifics
The 128-bit IPv6 address is written using 32 hexadecimal numbers.
The format is x:x:x:x:x:x:x:x, where x is a 16-bit hexadecimal field, therefore each x represents four hexadecimal digits.
Example address:
    2035:0001:2BC5:0000 : 0000:087C:0000:000A
Notes: The 128-bit address consists of 8, 16-bit segments, with each 16-bit segment represented by four Hex digits.
Each of the four hex digits is represents four bits.
A colon separates each set of four hex digits.
This is referred to as the “coloned hex” format whereas IPv4 notation is referred to as “dotted decimal”.
Hex digits are not case sensitive.
Note that IPv6 addresses currently being assigned by IANA for public use begin with Hex 2001.

## Slide 11: Abbreviating IPv6 Addresses
Leading 0s within each set of four hexadecimal digits can be omitted.
  09C0 = 9C0
  0000 = 0
A pair of colons (“::”) can be used, once within an address, to represent any number (“a bunch”) of successive zeros.
Notes: IPv6 addresses can be very long and confusing to look at.
Fortunately, in many cases, they can be abbreviated by suppressing leading zeros and representing 4 consecutive zeros within a 4-character Hex field with a single zero.
A pair of colons can be used to represent consecutive Hex field strings of zeros.
This greatly simplifies the writing of IPv6 addresses since the eight 16-bit Hex fields can be compressed when there are a number of consecutive zeros in the address. This happens frequently, especially with the network portion of the address.

## Slide 12: IPv6 Address Abbreviation Example
2031:0000:130F:0000:0000:09C0:876A:130B
2031:0000:130F:0000:0000:09C0:876A:130B
2031: 0:130F: 0: 0: 9C0:876A:130B
2031:0:130F:0:0:9C0:876A:130B
2031:0:130F:0:0:9C0:876A:130B
2031:0:130F::9C0:876A:130B
Notes: This example shows how an IPv6 address can be abbreviated or compressed by converting four hex digit zeros to a single zero, elimination of leading zeros and the representation of multiple sets of contiguous zeros as a double colon.
Remember that the double colon can be used only once in an IPv6 address.

## Slide 13: More IPv6 Address Abbreviation Examples
= FF01:0:0:0:0:0:0:1
= FF01::1
E3D7:0000:0000:0000:51F4:00C8:C0A8:6420
= E3D7::51F4:C8:C0A8:6420
3FFE:0501:0008:0000:0260:97FF:FE40:EFAB
= 3FFE:501:8:0:260:97FF:FE40:EFAB
= 3FFE:501:8::260:97FF:FE40:EFAB
FF01:0000:0000:0000:0000:0000:0000:1
Notes: Shown here are some additional examples of how IPv6 addresses with leading and contiguous zeros can be abbreviated.

## Slide 14: IPv6 Address Components
An IPv6 address consists of two parts:
  A subnet prefix
  An interface ID
IPv6 = 128 bits |  |  | 
11111111.11111111.11111111.11111111 | 11111111.11111111.11111111.11111111 | 11111111.11111111.11111111.11111111 | 11111111.11111111.11111111.11111111
Subnet prefix
Interface ID
Notes: The subnet prefix represents the network to which the interface is connected and is usually 64 bits in length.
The interface ID (sometimes called a local identifier) is also 64 bits in length.

## Slide 15: Subnet Prefix
The prefix length is almost always /64.
  However, IPv6 rules allow for either shorter or longer prefixes
Deploying a /64 IPv6 prefix on a device recommended.
  Allows Stateless Address Auto Configuration (SLAAC)
Notes: Deploying a /64 IPv6 prefix on a device recommended (pre-subscribed by RFC3177 (IAB/IESG Recommendations on IPv6 Address Allocations to Sites).
The major advantage to using a /64 prefix is that it allows Stateless Address Auto Configuration (SLAAC) as defined in RFC 2462.
Note that, although prefixes shorter than /64 can be assigned to a device (e.g., /60), it is considered bad practice and has no real application.

## Slide 16: Ethernet EUI-64 IPv6 Addresses
The first 64 bits are the network portion of the address and are statically specified or learned via SLAAC.
The interface ID (second 64-bits) is the host portion of the address and is automatically generated by the router or host device.
The interface ID on an Ethernet link is based on the 48-bit MAC address of the interface with an additional 16-bit 0xFFFE inserted in the middle of the MAC address.
Notes: With EUI-64 IPv6 addresses the first 64 bits are the network portion of the address and are either specified statically or learned via stateless autoconfiguration.
The interface ID (second 64-bits) is the host portion of the address and is automatically generated by the router or host device.
The interface ID on an Ethernet link is based on the 48-bit MAC address of the interface with an additional 16-bit 0xFFFE inserted in the middle of the MAC address.
This creates an extended unique identifier referred to as the EUI-64 format.
EUI-64 addresses can be generated on IPv6 router interfaces and on IPv6 hosts.

## Slide 17: EUI-64 IPv6 Interface Identifier
48-bit MAC Address
64-bit IPv6 EUI-64 Interface ID
Notes: The EUI-64 standard inserts a 16-bit Hex value FFFE in the middle at the 24th bit of the MAC address to create a unique 64-bit interface identifier.
The seventh bit in the high-order byte is set to 1 to indicate the uniqueness of the interface ID.

## Slide 18: IPv6 Address Types
Address Type | Description | Topology
Unicast | “One to One” An address destined for a single interface. A packet sent to a unicast address is delivered to the interface identified by that address. | 
Multicast | “One to Many” An address for a set of interfaces (typically belonging to different nodes). A packet sent to a multicast address will be delivered to all interfaces identified by that address. | 
Anycast | “One to Nearest” (Allocated from Unicast) An address for a set of interfaces. In most cases these interfaces belong to different nodes. created “automatically” when a single unicast address is assigned to more than one interface. A packet sent to an anycast address is delivered to the closest interface as determined by the IGP. | 
Notes: There are three main groups or addresses types defined for use with IPv6.
IPv6 Unicast and Multicast addresses perform a similar function as those in IPv4.
The Anycast type of address is new to IPv6 and not widely used at this time.
Anycast can be used by routers to facilitate load sharing and provide alternate path flexibility if a router becomes unavailable. Only routers should respond to an anycast address.
Recall that with IPv6 there are no broadcasts and no broadcast addresses.

## Slide 19: IPv6 Unicast Address Scopes
Address types have well-defined destination scopes:
  Link-local address
  Site-local address (replaced by Unique-local addresses)
  Global unicast address
Link-Local
Site-Local
Global
(Internet)
Note: Site-Local Address are deprecated in RFC 3879.
Notes: There are three main categories of unicast addresses with IPv6, each of which has a different focus or scope.
These were originally defined as Link-Local, Site-Local and Global.
However, with RFC 3879, Site-Local Addresses are deprecated (not supported) and have been replaced by Unique-Local addresses.

## Slide 20: Site-Local Addresses - Deprecated
Site-local addresses allowed devices in the same organization, or site, to exchange data.
  Site-local addresses start with the prefix FEC0::/10.
They are analogous to IPv4's private address classes.
    However, using them would also mean that NAT would be required and addresses would again not be end-to-end.
Site-local addresses are no longer supported (deprecated by RFC 3879).
Notes:   Site-local addresses, mentioned previously, have been deprecated.
  They are analogous to IPv4's private address classes. However, using them would also mean that NAT would be required and addresses would again not be end-to-end.
  Site-local addresses start with the prefix FEC0::/10 and are still commonly used in training literature.
  Unique-local addresses (those in address block FC00::/7) have replaced the Site-local addresses for use with systems that are not connected to the Internet. They are routable only within a private network and are not routable in the global IPv6 Internet.

## Slide 21: IPv6 Unicast Address Scopes
Link-local addresses—only on single link, not routed
  FE80 prefix
Unique-local addresses—routed within private network
  FC00 prefix
Global unicast addresses—globally routable
  2001 prefix most common
Notes: Link-local addresses are only configured on a single link between two devices. They are not routed and always start with a FE80 prefix. They are commonly used for IGP routing protocol communication.
Unique-local addresses are routable, but only within a private network, they are not supported on the Internet and are not to be used with NAT. They always start with a FC00 prefix.
Global unicast addresses are globally routable on the Internet. The 2001 prefix is currently being issued by IANA for public use. Global unicast addresses always contain a 64-bit host portion. They are identified by their three high-level bits set to 001 (hex 2 or 3::/3). 0010 = 0x2 & 0011 = 0x3.
These three types of IPv6 unicast address are easily identified by their prefix.

## Slide 22: Multiple IPv6 Addresses per Interface
An interface can have multiple global IPv6 addresses.
Typically, an interface is assigned a link-local and one (or more) global IPv6 address.
For example, an Ethernet interface can have:
    Link-local address
    (FE80::21B:D5FF:FE5B:A408)
    Global unicast address
    (2001:8:85A3:4289:21B:D5FF:FE5B:A408)
The Link-local address is used for local device communication.
The Global address is used to provide Internet reachability.
Notes: An interface can have multiple IPv6 global unicast addresses simultaneously configured and enabled on it. However, it must also have a single link-local address.
Typically, an interface is assigned a link-local address and one (or more) global IPv6 addresses.
Note that in the example, the Link Local address starts with Hex FE80 and the global unicast address starts with Hex 2001.
Both of these addresses were autoconfigured using the EUI-64 method which makes use of the Ethernet MAC address to create the interface ID (in this example, 21B:D5FF:FE5B:A408). Autoconfiguration and EUI-64 are covered in IPv6 Intro Part 2.
An interface could also be configured to simultaneously support IPv4 and IPv6 addresses. This creates a “dual-stacked” interface.